## Slide 1
<IRC-2026_Abstract ID>
A Gamified Upper Limb Stroke Rehabilitation System with Remote Monitoring and Communication Features
A.F.M. Imzan1*, M.N.M. Atheeq1, Dulashi Karunakalage2, H M V M N Herath1
1Dept. of Electronics & Telecommunication, SLTC, Padukka, Sri Lanka 2Dept. of Electrical Engineering, SLTC, Padukka, Sri Lanka *22ug2-0072@sltc.ac.lk
Introduction
Most stroke survivors keep lasting arm and hand impairment [1]. Repeated practice is needed, but patients lose interest and lack therapists [2].
Games make practice engaging [3]
Few systems also add EMG and remote therapist support
Research Objectives
To sense forearm EMG and hand motion
To recognize 7 hand/wrist movements
To build games and a therapist web app
Methodology
An ESP32 samples an MD0437 forearm EMG envelope at 1 kHz; MediaPipe [4] maps webcam hand landmarks to 7 movements. Every 50 ms, fusion attaches 8 EMG features to each camera command (Figure 01). Classifiers and MOMENT-1 [5] were compared offline on 9 healthy volunteers.
Figure 01: System architecture
Results and Discussions
Frozen MOMENT-1 features with a random forest were best: 48.1% LOSO accuracy (chance 14.3%).
Table 01: Seven-movement accuracy
Method | LOSO | Holdout
SVM, 200 ms | 37.2% | 40.5%
SVM, 5.12 s | 47.3% | 50.2%
MOMENT-1 LoRA | 43.2% | 45.5%
Frozen MOMENT-1 + RF | 48.1% | 49.3%
Source: nine healthy volunteers; RF = random forest
Acknowledgement
We thank our EMG volunteers.
Figure 02: LOSO recall per movement (S02–S09)
One EMG channel shows effort, not direction, so the camera decides moves.
Conclusions
Low-cost prototype works end to end
EMG best gives activity feedback
Next: Wi-Fi, messaging, stroke pilot
References
[1] GBD 2021 Stroke Risk Factor Collaborators, Lancet Neurol., vol. 23, no. 10, pp. 973–1003, 2024.
[2] C. Winstein and R. Varghese, NeuroRehabilitation, vol. 43, no. 1, pp. 3–18, 2018.
[3] I. Doumas et al., J. NeuroEng. Rehabil., vol. 18, no. 1, Art. no. 100, 2021.
[4] F. Zhang et al., “MediaPipe Hands,” arXiv:2006.10214, 2020.
[5] M. Goswami et al., “MOMENT,” in Proc. ICML, 2024.
EMG + ESP32
1 kHz, 8 features
Webcam
MediaPipe, 7 labels
Fusion engine
every 50 ms
Four games
adaptive difficulty
RehabHub
FastAPI + SQLite
Chart: Recall (%)
| Rest | Open | Close | Left | Right | Up | Down
SVM, 200 ms | 81 | 46 | 66 | 23 | 9 | 19 | 11
MOMENT-1 + RF | 78 | 74 | 75 | 40 | 31 | 9 | 27
Notes: On-screen poster (16:9, 13.33 x 7.5 in). Verdana throughout. Title 30 pt bold (may shrink to fit); presenting author 14 pt underlined; affiliations 11 pt; section headings 16 pt bold; body 12 pt; captions 11 pt (Table 01: / Figure 01: / Image 01:); table body 10 pt; sources and references 9 pt. Do not go below these sizes - cut words instead. The layout is flexible: boxes may be resized, moved or rearranged and extra figures, tables or images added (Table 02, Figure 03, Image 02...), as long as all section headings remain and the minimum sizes are kept.